## Slide 1
Using CMF’s in Benefit/Cost Analysis and Project Prioritization
December 8, 2015
Presented by
Michael McNeill, P.E.
ODOT Safety Program

## Slide 2
ODOT Safety Application Process / Project Prioritization
Explain how ODOT staff integrates the CMF Clearinghouse
Overview
Recommendations for best using the Clearinghouse and countermeasure selection
Discuss the ODOT Safety Application Process and how CMFs are used within it
Expand on this process to include how CMFs are applied

## Slide 3
ODOT Safety Application Process
Safety Projects developed the following ways:
Application Process
Applications are submitted through the ODOT Districts to Central Office. (12 ODOT Districts)
-ODOT Priority Lists
-ODOT Sponsored
-Local Sponsored
Multi-disciplinary ODOT Safety Review Committee reviews all applications once submitted
Consists of Safety Program, Traffic Engineering, Roadway Engineering, Local Programs

## Slide 4
ODOT Safety Application Process / Project Prioritization
Application Process Flow Chart
Safety Location Chosen
(ODOT District or Local)
Crash Data Collected & Analyzed
Countermeasures Selected
ECAT Completed
CMF’s are applied within this tool.
Safety Application completed and submitted
Safety Committee Reviews application for funding

## Slide 5
How is a location chosen?
Projects developed the following ways:
1) ODOT Priority Lists
Rural Intersection
Rural Segment – Non Freeway
Rural Freeway
Urban Intersection
Urban Segment – Non Freeway
Urban Freeway
2) ODOT Sponsored – District
3) Local Sponsored – County, Municipality, etc.
Local routes not on priority list
Safety Location Chosen
Notes: Safety Location chosen

## Slide 6
GCAT – What’s the crash patterns?
Crash Data Collected & Analyzed
Notes: Crash Data Collected and Analyzed

## Slide 7
What’s the best countermeasure that will address the crash problems for the lowest cost?
Select Countermeasures
57 Rear End crashes from 2006-2010
Install Dedicated Left Turn Lane?

## Slide 8
Economic Crash Analysis Tool
ECAT Analysis
Imports crash data from GCAT
Calculates predicted crash frequencies and provides a value for the potential for safety improvement
Notes: This goes through all of the background calculations seen in the HSM. Takes into account crashes, site type, and provides a net present value of how much the safety benefits are worth for the project. This amount is then compared against the total cost of the countermeasures (as seen in the red box) to yield a Benefit/Cost Ratio.

## Slide 9
Economic Crash Analysis Tool
Tool has the ability to complete a benefit-cost analysis
ECAT Analysis

## Slide 10
Tab dedicated to CMF selection
CMF Table in ECAT
All information obtained from the Highway Safety Manual and the CMF Clearinghouse
Economic Crash Analysis Tool
Nearly 60 preloaded CMF’s available for selection
CMF ID’s
Site Type
Countermeasure Name
Suggested Service Life
Star Quality Rating (3 is ODOT’s Minimum)
CMF associated with specific crash type
If countermeasure is not on preloaded list, the CMF clearinghouse can then be referenced and used with the 3 star minimum

## Slide 11
CMF Table in ECAT
Economic Crash Analysis Tool
Countermeasure names link to research reports

## Slide 12
CMF Table in ECAT
How are the modification factors correctly assigned?
If CMF states crash type ‘All’, then it has a
value applied to the severity only.
B) If designed for a specific crash type, each of
those is listed with the corresponding injury
severity

## Slide 13
Items included in submission of a safety project application
Safety Application Review Committee
A) Electronic copy of the Safety Engineering Study
B) All Excel file analysis
1) CAM Tool (Crash data generated from GCAT)
2) ECAT Tool (Displays countermeasures/CMFs and Benefit/Cost)
3) Safety Application and Scoring Tool
C) District Approval Signatures
Committee reviews project applications

## Slide 14
Decisions are most effective when developed through a data driven process.
-Valid research backing these CMF’s
Recommendations
Visit CMF Clearinghouse for reference materials
-Search for CMF’s
1) User Guide - http://www.cmfclearinghouse.org/userguide.cfm
2) FAQ’s - http://www.cmfclearinghouse.org/faqs.cfm
Friends don’t let friends use bad data!
Notes: Since they gave me the final slot of the day, I wanted to drive home some key points as seen throughout the presentations today.

## Slide 15
Reference Materials
http://www.dot.state.oh.us/Divisions/Planning/ProgramManagement/HighwaySafety/HSIP/Pages/ECAT.aspx
Website features
Background Information
ECAT File
  CMF Tab
Several Examples provided
Notes: Oregon DOT has provided a website on how they use CMF’s along with many The link for that is included in the FAQ’s section on the CMF clearinghouse as mentioned in the previous slide.

## Slide 16
Questions?
What’s the CMF for Highway Lighting?